## Slide 1: FNAL beam test simulation with Geant4.10.01
Aiwu Zhang
Florida Tech
2015-01-20

## Slide 2: Geant4 geometry
All materials (mylar, Al drift, Cu/Ni/Au r/o, G10, FR4, Ar/CO2, etc…) are implemented. HoneyComb is replaced by 0.1mm mylar film. GEM holes are not implemented. No r/o strips.
Origin is in the center.
Input particle is set to be a point beam, normal incident, 20 mm in front of REF1.
Physics list used is FTFP_BERT:
http://geant4.cern.ch/support/proc_mod_catalog/physics_lists/hadronic/FTFP_BERT.html
In which Multiple Scattering model (based on the Lewis theory) is included:
http://geant4.cern.ch/G4UsersDocuments/UsersGuides/PhysicsReferenceManual/html/node34.html
No resolution smearing on the detectors. The results will reflect the “intrinsic” resolutions.

## Slide 3
What are studied at the first step:
Build exclusive and inclusive residuals for: (1) four trackers (2) FITEIC, in Cartesian coordinates.
Compared: [ 32GeV/c , 120GeV/c ] [pi- , proton]
20k events are simulated for each run.
The plots in X coordinate will be shown in the following. (plots in Y are very similar). Both resolutions will be shown in tables.

## Slide 4: 32GeV/c pi- position distributions
REF1X
REF2X
REF3X
REF4X
FIT_EIC_X
Divergence of the ‘beam’ is clear.
Units in all plots are in mm.

## Slide 5: 120GeV/c pi- position distributions
REF1X
REF2X
REF3X
REF4X
FIT_EIC_X
Divergence of the ‘beam’ is much smaller than the 32GeV/c case.
Units in all plots are in mm.

## Slide 6: 32GeV/c proton position distributions
REF1X
REF2X
REF3X
REF4X
FIT_EIC_X
Divergence of the ‘beam’ is clear and very similar to the 32GeV/c Pions.
Units in all plots are in mm.

## Slide 7: 120GeV/c proton position distributions
REF1X
REF2X
REF3X
REF4X
FIT_EIC_X
Divergence of the ‘beam’ is much smaller than the 32GeV/c case. Similar to the 120GeV/c pion case
Units in all plots are in mm.

## Slide 8: 32GeV/c pi- residual distributions
REF1X
Exclusive
REF1X
Inclusive
Units all in um
REF2X
Exclusive
REF2X
Inclusive
GeoMean: 45um
GeoMean: 39um

## Slide 9: 32GeV/c pi- residual distributions
REF3X
Exclusive
REF3X
Inclusive
Units all in um
REF4X
Exclusive
REF4X
Inclusive
GeoMean: 26um
GeoMean: 41um

## Slide 10: 32GeV/c pi- residual distributions for FITEIC
FITEIC_X
Exclusive
FITEIC_X
Inclusive
Units all in um
FITEIC_Y
Exclusive
FITEIC_Y
Inclusive
GeoMean: 56um
GeoMean: 56um

## Slide 11: 120GeV/c pi- residual distributions
REF1X
Exclusive
REF1X
Inclusive
Units all in um
REF2X
Exclusive
REF2X
Inclusive
GeoMean: 12um
GeoMean: 10um

## Slide 12: 120GeV/c pi- residual distributions
REF3X
Exclusive
REF3X
Inclusive
Units all in um
REF4X
Exclusive
REF4X
Inclusive
GeoMean: 7um
GeoMean: 11um

## Slide 13: 120GeV/c pi- residual distributions for FITEIC
FITEIC_X
Exclusive
FITEIC_X
Inclusive
Units all in um
FITEIC_Y
Exclusive
FITEIC_Y
Inclusive
GeoMean: 15um
GeoMean: 15um

## Slide 14: Comparison tables
 | 32GeV/c pi- |  |  |  |  |  | 120GeV/c pi- |  |  |  |  | 
 | Ex | Ex_err | In | In_err | GM | GM_err | Ex | Ex_err | In | In_err | GM | GM_err
REF1X | 86 | 0.5 | 23 | 0.1 | 45 | 0.4 | 23 | 0.1 | 6 | 0.0 | 12 | 0.1
REF1Y | 87 | 0.5 | 24 | 0.1 | 45 | 0.4 | 24 | 0.1 | 6 | 0.0 | 12 | 0.1
REF2X | 46 | 0.3 | 32 | 0.2 | 39 | 0.3 | 13 | 0.1 | 9 | 0.1 | 10 | 0.1
REF2Y | 47 | 0.3 | 33 | 0.2 | 39 | 0.3 | 13 | 0.1 | 9 | 0.1 | 11 | 0.1
REF3X | 33 | 0.2 | 20 | 0.1 | 26 | 0.2 | 9 | 0.1 | 6 | 0.0 | 7 | 0.1
REF3Y | 33 | 0.2 | 20 | 0.1 | 26 | 0.2 | 9 | 0.1 | 6 | 0.0 | 7 | 0.1
REF4X | 63 | 0.4 | 27 | 0.2 | 41 | 0.3 | 17 | 0.1 | 7 | 0.0 | 11 | 0.1
REF4Y | 63 | 0.4 | 28 | 0.2 | 42 | 0.3 | 17 | 0.1 | 7 | 0.0 | 11 | 0.1
FITEIC_X | 63 | 0.4 | 49 | 0.3 | 56 | 0.5 | 17 | 0.1 | 13 | 0.1 | 15 | 0.1
FITEIC_Y | 63 | 0.4 | 50 | 0.3 | 56 | 0.5 | 17 | 0.1 | 14 | 0.1 | 15 | 0.1
 | 32GeV/c proton |  |  |  |  |  | 120GeV/c proton |  |  |  |  | 
REF1X | 87 | 0.5 | 23 | 0.1 | 45 | 0.4 | 23 | 0.1 | 6 | 0.0 | 12 | 0.1
REF1Y | 86 | 0.5 | 23 | 0.1 | 44 | 0.4 | 23 | 0.1 | 6 | 0.0 | 12 | 0.1
REF2X | 47 | 0.3 | 33 | 0.2 | 39 | 0.3 | 12 | 0.1 | 9 | 0.1 | 10 | 0.1
REF2Y | 46 | 0.3 | 32 | 0.2 | 39 | 0.3 | 13 | 0.1 | 9 | 0.1 | 10 | 0.1
REF3X | 33 | 0.2 | 20 | 0.1 | 26 | 0.2 | 9 | 0.1 | 5 | 0.0 | 7 | 0.1
REF3Y | 33 | 0.2 | 20 | 0.1 | 26 | 0.2 | 9 | 0.1 | 5 | 0.0 | 7 | 0.1
REF4X | 63 | 0.4 | 28 | 0.2 | 42 | 0.4 | 17 | 0.1 | 7 | 0.0 | 11 | 0.1
REF4Y | 62 | 0.4 | 27 | 0.2 | 41 | 0.3 | 17 | 0.1 | 7 | 0.0 | 11 | 0.1
FITEIC_X | 63 | 0.4 | 50 | 0.3 | 56 | 0.5 | 17 | 0.1 | 13 | 0.1 | 15 | 0.1
FITEIC_Y | 62 | 0.4 | 49 | 0.3 | 55 | 0.5 | 17 | 0.1 | 13 | 0.1 | 15 | 0.1
Units in um

## Slide 15: Resolutions for trackers
 |  | Ex_exp | In_exp | GM_exp | Ex_G4 | In_G4 | GM_G4 | Corrected resolution
32GeV/c pion case | REF1X | 164 | 44 | 86 | 86 | 23 | 45 | 73
 | REF1Y | 166 | 45 | 87 | 87 | 24 | 45 | 74
 | REF2X | 95 | 66 | 79 | 46 | 32 | 39 | 69
 | REF2Y | 97 | 68 | 81 | 47 | 33 | 39 | 71
 | REF3X | 82 | 50 | 64 | 33 | 20 | 26 | 59
 | REF3Y | 82 | 50 | 64 | 33 | 20 | 26 | 58
 | REF4X | 126 | 55 | 83 | 63 | 27 | 41 | 72
 | REF4Y | 118 | 51 | 78 | 63 | 28 | 42 | 65
 |  | Ex_exp | In_exp | GM_exp | Ex_G4 | In_G4 | GM_G4 | 
120 GeV/c proton | REF1X | 134 | 36 | 70 | 23 | 6 | 12 | 69
 | REF1Y | 98 | 27 | 52 | 23 | 6 | 12 | 50
 | REF2X | 77 | 54 | 65 | 12 | 9 | 10 | 64
 | REF2Y | 62 | 43 | 52 | 13 | 9 | 10 | 51
 | REF3X | 68 | 42 | 54 | 9 | 5 | 7 | 53
 | REF3Y | 74 | 45 | 58 | 9 | 5 | 7 | 58
 | REF4X | 91 | 41 | 61 | 17 | 7 | 11 | 60
 | REF4Y | 93 | 40 | 61 | 17 | 7 | 11 | 60
“Corrected resolution” means calculate resolution in quadrature: .

## Slide 16: Resolutions for FIT EIC chamber (zigzag)
In the beam data we analyze in polar coordinate and get a resolution ~170urad, at R=1870mm.
The G4 simulation shows that resolution on the FITEIC chamber is 56um, which is 56/1.87urad=30urad if we transfer it into polar coordinates.
So, the corrected resolution for the zigzag chamber is : .

## Slide 17: Scattering angles
Polar angle:
Azimuthal angle:
Polar angle reflects the divergence of ‘beam’, ie., the scattering effect.
The polar angle is also dependent on the distance between detectors.

## Slide 18
Pi-, 32GeV/c
Rho between REF2 and REF1
Pi-, 120GeV/c
Rho between REF2 and REF1
Pi-, 32GeV/c
Rho between REF4 and REF1
Pi-, 120GeV/c
Rho between REF4 and REF1
Pi-, 32GeV/c
Rho between
REF4 and REF3
Pi-, 120GeV/c
Rho between
REF4 and REF3
Rho

## Slide 19
Pi-, 32GeV/c
theta between
REF2 and REF1
Pi-, 120GeV/c
theta between
REF2 and REF1
Pi-, 32GeV/c
theta between
REF4 and REF1
Pi-, 120GeV/c
theta between
REF4 and REF1
Pi-, 32GeV/c
theta between
REF4 and REF3
Pi-, 120GeV/c
theta between
REF4 and REF3
Theta

## Slide 20
Rho angles | unit in urad |  |  |  |  | 
 | REF2-REF1 |  | REF4-REF1 |  | REF4-REF3 | 
 | mean | rms | mean | rms | mean | rms
32GeV/c pi- | 34 | 27 | 76 | 50 | 186 | 107
120GeV/c pi- | 9 | 11 | 23 | 32 | 54 | 46
32GeV/c proton | 33 | 26 | 76 | 51 | 184 | 106
120GeV/c proton | 9 | 10 | 24 | 37 | 55 | 54
Comparison tables
Summary
Geant4 simulation can produce “intrinsic” resolutions for the FNAL trackers and the FIT EIC chamber. At 32GeV/c, FIT EIC chamber gives resolution of ~56um.
The zigzag GEM resolution after the multiple scattering correction is .
Total Scattering angle for 32GeV/c is around 76urad, with a rms width 50urad.
Further studies can be done with this G4 simulation package, such as efficiency (>99% estimation).